## Slide 1
Computer Architecture
Assignment #1: ARM Instructions Analysis
Gyu Dong Kim (gyudong_kim@korea.ac.kr)

## Slide 2: Binary number
Binary number represents any number with 0 and 1
How to convert Decimal to Binary?
  7392 = 7 × 103 + 3 × 102 + 9 × 101 +2 × 100
How to convert binary to Decimal?
  (11010)2 =1×24+1×23+0×22+1×21+0×20 = (26)10
210
220
230
= 1Kilo
= 1Mega
= 1Giga

## Slide 3: Convert to binary
Ex 1-1) Convert decimal 41 to binary.
answer : (41)10 = (a5a4a3a2a1a0)2 = (101001)2
 | Integer Quotient |  | Remainder | Coefficient
41/2 = | 20 | + | ½ | a0 = 1
20/2 = | 10 | + | 0 | a1 = 0
10/2 = | 5 | + | 0 | a2 = 0
5/2 = | 2 | + | ½ | a3 = 1
2/2 = | 1 | + | 0 | a4 = 0
1/2 = | 0 | + | ½ | a5 = 1
Integer | Remainder
41 | 
20 | 1
10 | 0
5 | 0
2 | 1
1 | 0
0 | 1
Answer
=101001

## Slide 4: Octal and Hexadecimal

## Slide 5: #’s complement
(r-1)’s complement of N is (rn-1) - N
  n is equal to N’s digit
r=10, r-1=9, the 9’s complements of N is (10n - 1) - N
Ex) the 9’s complements of 546700 is 999999 (= 1000000 – 1) -546700 = 453299
the 9’s complements of 012398 is 999999-012398 = 987601
In the case of binary, r=2, r-1=1 1’s complement of N is (2n - 1) - N
Ex) the 1’s complements of 1011000 is (10000000 – 1) - 1011000 = 1111111 – 1011000 = 0100111
the 1’s complements of 0101101 is 1010010

## Slide 6: #’s complement
rn-N = [(rn-1)-N] + 1
  r’s complements is equal to (r-1)’s complements + 1
Ex) the 2’s complements of 1011000 is 0100111 + 1 = 0101000
the 2’s complements of 0101101 is 1010010 + 1 = 1010011

## Slide 7: #’s complement
Ex1-7) X=1010100, Y=1000011, (a) X-Y, (b) Y-X
X = | 1010100
2’s complement of Y = | +0111101
Sum = | 10010001
Discard end carry 27 = | -10000000
Answer: X-Y = | 0010001
Y = | 1000011
2’s complement of X = | +0101100
Sum = | 1101111
There is no carry.
The answer is Y-X = -(2’s complement of 1101111)=-0010001

## Slide 8: #’s complement
Ex) X=1010100, Y=1010100, X-Y
X = | 1010100
2’s complement of Y = | +0101100
Sum = | 10000000
Discard end carry 27 = | -10000000
Answer: X-Y = | 0000000
The answer is X-Y = 0

## Slide 9: Shift operation in binary
(11010)2 =1×24+1×23+0×22+1×21+0×20 = (26)10
Shift Left 2
(1101000)2 = 1 x 26 + 1 x 25 + 0 x 24 + 1 x 23 + 0 x 22 + 0 x 21 + 0 X 20
= (104)10 = (26)10 x 4
(110100)2 = 1×25+1×24+0×23+1×22+0×21+0×20 = (52)10
Shift Right 2
(1101)2 = 1×23+1×22+0×21+1×20 = (13)10 = (52)10 / 4

## Slide 10: inst_data.mif
Word
Index
Instruction
EA000006
Byte
Address
0
4
8
12…20
24
28
36
40
.
.
.

## Slide 11: Example
000: EA000006
  Change instructions to binary format
    1110 1010 0000 0000 0000 0000 0000 0110 (2)
  Translate the binary instructions to assembly codes by referring to the reference file
    B #008;
  Describe what instruction means
    1. Sign-extending the 24-bit signed (two’s complement) immediate to 30 bits
      0000 0000 0000 0000 0000 0110 -> 00 0000 0000 0000 0000 0000 0000 0110
    2. Shifting the result left two bits to form a 32-bit value
      0000 0000 0000 0000 0000 0000 0001 1000 = 610 * 4 = 2410
    Adding this to the contents of the PC, which contains the address of the branch instruction plus 8 bytes.
      Make ‘32’ by adding the current instruction address ‘(0*4)+8’ and ‘24’
      Divide ‘32’ into 4 so that it branches at first among the word-unit instructions : 32 / 4 = 8
      Next instruction will be E59F2EC8 at the address 008

## Slide 12: Example
001: EAFFFFFE
  Change instructions to binary format
    1110 1010 1111 1111 1111 1111 1111 1110 (2)
  Translate the binary instructions to assembly codes by referring to the reference file
    B #001;
  Describe what instruction means
    1. Sign-extending the 24-bit signed (two’s complement) immediate to 30 bits
      1111 1111 1111 1111 1111 1110 -> 11 1111 1111 1111 1111 1111 1111 1110
    2. Shifting the result left two bits to form a 32-bit value
      1111 1111 1111 1111 1111 1111 11111 1000 = -210 * 4 = -810
    Adding this to the contents of the PC, which contains the address of the branch instruction plus 8 bytes.
      Make ‘4’ by adding the current instruction address ‘(1*4)+8’ and ‘-8’
      Divide '4' into 4 so that it branches at first among the word-unit instructions : 4/4 = 1
      Because it branches to the same instruction, the same instruction repeats indefinitely
1111 1111 1111 1111 1111 1110 = 2’s complement of 0000 0000 0000 0000 0000 0010