## Slide 1: Lecture 00 Data Communications
Basic Concepts
Data Communication and Layering

## Slide 2: References
Books
  Data Communications and Network, 6th, Behrouz A. FORIUZAN, McGraw-Hill
  Data and Computer Communications, 9th, William Stallings, Pearson Education, Prentice Hall
Standards
  IEEE 802, IETF RFC
Web sites
  Wikipedia, etc

## Slide 3: Contents
Data Communication
  Definition
  Data
  Communication
Layering and Reference Model
  ISO OSI 7-layer reference model
  IEEE 802 Reference Model

## Slide 4: Data Communication
Definition

## Slide 5: Data Communications Definition
Data communications are the exchange of data between two devices via some form of transmission media
The Mathematical Theory of Communication
  The fundamental problem of communication is that of reproducing at one point either exactly or approximately a message selected at another point.

## Slide 6: Data Communication
Data

## Slide 7: Data Communications Data and Data Standards
Digital Data
  Text : Characters
  Numbers
Audio
  Voice (Speech) : Phone
  Music
  Sound
Image
  Still Image (Photo, Drawings)
  Moving Picture (Movie): real-time or non-real-time

## Slide 8: Data Communications Data Standards : Characters
Unicode encoding model
  character repertoire
    the full set of abstract characters that a system supports
  coded character set (CCS; U+0000 to U+10FFFF [17 planes])
    a function that maps characters to code points
      each code point represents one character
      Basic Multilingual Plane (BMP; plane 0) : U+0000 to U+FFFF
        CJK Unified Ideographs (4E00–9FFF)
  character encoding form (CEF)
    the mapping of code points to code units to facilitate storage in a system that represents numbers as bit sequences of fixed length
      For example, a system that stores numeric information in 16-bit units can only directly represent code points 0 to 65,535 in each unit, but larger code points (say, 65,536 to 1.4 million) could be represented by using multiple 16-bit units
  character encoding scheme (CES)
    the mapping of code units to a sequence of octets to facilitate storage on an octet-based file system or transmission over an octet-based network
      Unicode Transformation Format (UTF-8, UTF-16BE, UTF-32B)

## Slide 9: Data Communications Data Standards : Numbers
Integers
  Sign-magnitude, (sign:-(1),+(0))(magnitude)
    (1)(11):(-3)..(1)(00):(-0),(0)(00):(+0)..(0)(11):(+3)
    (-0)+(+0)=100+000=100 (-0), (-3)+(+3)=111+011=(1)010 (??)
  One’s complement (-n..-0,+0..n)
    100:(-3),101:(-2),110:(-1),111:(-1),000:(+0)..011:(+3))
    (-0)+(+0)=111+000=111 (-0), (-3)+(+3)=100+011=111 (-0)
    (-3)+(+1)=011+001 = 100 (-3)?? Overflow
    (-1)+(+2)=110+010 = (1)(000)=>adding the carry bit: 000+(1) = 001
    111:(0) 110:(-1) 101:(-2) 100:(-3)
  Two’s complement (-n..-1,0..n-1)
    100:(-4) 101:(-3),110:(-2),111:(-1),000:(0)..011:(+3))
    (-1)+(+2)=111+010 =(1)001 (discarding the carry bit)

## Slide 10: Data Communications Data Standards : Numbers
Real Numbers (Floating points)
  IEEE Standard for Floating-Point Arithmetic (IEEE 754)
    Finite number : (−1)s × c × bq
      described by three integers:
        s = a sign (zero or one),
        c = a Significand precision (or 'coefficient’),
        q = an exponent
      c must be normalized value to the form: 1.xxxxx (0.0101→1.0100 ()
      q is also a signed integer.
        It use biased exponent (the bias (127(0x7F)/1023(0x3FF)/16383(0x3FFF))
    Two infinities: +∞ and −∞; NaN

## Slide 11: Data Communications Data Standards : Numbers
Real Numbers (Floating points)
  IEEE Standard for Floating-Point Arithmetic (IEEE 754)
    Single (4-octets)/Double (8-octets)/Quadruple (16-octets) precision

## Slide 12: Data Communications Data Standards : Numbers
Real Numbers (Floating points)
  IEEE Standard for Floating-Point Arithmetic (IEEE 754)
    The two exponents are interpreted specially.
      0x00(8bits)/0x000(11bits)/0x0000(15bits):
        . ()
      0xFF(8bits)/0x7FF(11bits)/0x7FFF(15bits):NaN()

## Slide 13: Data Communications Data Standards : Image
Image file formats
  Raster graphics or bitmap image :
    the data describes the characteristics of each individual pixel
    JPEG(Joint Photographic Experts Group)
    GIF (Graphics Interchange Format)
    PNG (Portable Network Graphics)
      open-source alternative to GIF
  Vector formats :
    a geometric description which can be rendered smoothly at any desired display size
    SVG (Scalable Vector Graphics)
      an open standard by the World Wide Web Consortium

## Slide 14: Data Communications Data Standards : Video
Moving Picture Experts Group (MPEG)
  a working group of ISO/IEC with the mission to develop standards for coded representation of digital audio and video and related data
    MPEG-2 : Transport, video and audio standards for broadcast-quality television
    MPEG-4 Part 2 (MPEG-4 Visual) : a video compression format
      DivX, Xvid and Nero Digital
    MPEG-4 Part 3 (MPEG-4 Audio) : audio coding methods
      Speech coding – HVXC (Harmonic Vector eXcitation Coding)
      Speech coding – CELP (Code Excited Linear Prediction)
      General Audio Coding (GA) - Advanced Audio Coding (AAC)
    MPEG-4 Part 10, Advanced Video Coding (MPEG-4 AVC) : a block-oriented motion-compensation-based video compression standard

## Slide 15: Data Communications Data Description Standards : Audio
Non-compression
  Linear pulse-code modulation (LPCM, PCM)
  Pulse-density modulation (PDM)
Lossless compression
  Free Lossless Audio Codec (FLAC)
  Apple Lossless Audio Codec (ALAC)
Lossy compression
  Discrete cosine transform (DCT)
Adaptive Multi-Rate audio codec
  an audio compression format optimized for speech coding
  The standard speech codec by 3GPP

## Slide 16: Data Communications Data Description Standards : Media Type
Media type (email/MIME, HTTP)
  (RFC2046) Multipurpose Internet Mail Extensions (MIME) Part Two: Media Types
    (RFC2045) Multipurpose Internet Mail Extensions (MIME) Part One: Format of Internet Message Bodies
  A two-part identifier for file formats and format contents transmitted on the Internet

## Slide 17: Data Communications Data Description Standards : Media Type
Media type (email/MIME, HTTP)
  Top-level type name / subtype name [ ; parameters ]
    text/plain; charset=UTF-8
    audio/mpeg
    image/png
    image/jpeg
  The currently registered top-level type names are:
    application, audio, example, font, image, message, model,
    multipart, text, video.

## Slide 18: Data Communications Data Description Standards : AVP
Audio video profile
  RTP audio/video profile (RTP/AVP)
    It specifies a mapping of specific audio and video codecs and their sampling rates to RTP payload types and clock rates, and how to encode each data format as an RTP data payload, as well as specifying how to describe these mappings using Session Description Protocol (SDP)
    (RFC3550) RTP: A Transport Protocol for Real-Time Applications
      the real-time transport protocol (RTP)
      the RTP control protocol (RTCP)
    (RFC3551) RTP Profile for Audio and Video Conferences with Minimal Control
    (RFC4566) SDP: Session Description Protocol

## Slide 19: Data Communication
Communication

## Slide 20: Data Communications Components
Five Components

## Slide 21: Protocol : definition
A protocol defines the rules that both the sender and receiver, and all intermediate devices need to follow to be able to communicate effectively

## Slide 22: Protocol : the rules message format, order, actions
protocols define format, order of messages sent and received among network entities, and actions taken on messages transmission, receipt
(format, order)
  (action)
  The module implementing the protocol

## Slide 23: Protocol : Sending a letter
Write the letter you want to send
Buy an envelope and a post stamp
Insert the letter into the envelope
Write the receiver’s name, address and postcode at the right bottom corner of the envelope
Write the sender’s name, address and postcode at the left upper corner of the envelope
Attach the post stamp to the envelope
Put the envelop into the postbox
Why do you stick this procedure?

## Slide 24: Layering

## Slide 25: Data Communications ISO OSI reference model
OSI (Open Systems Interconnection) reference model
  A conceptual model that characterizes and standardizes the communication functions of a telecommunication or computing system without regard to their underlying internal structure and technology
International Organization for Standardization (ISO)
  ISO/IEC 7498-1:1994 - Basic Reference Model

## Slide 26: Data Communications ISO OSI reference model
Its goal is the interoperability of diverse communication systems with standard protocols
The model partitions a communication system into abstraction layers
  The original version of the model defined seven layers

## Slide 27: Data Communications Principles of protocol layering
Two principles of protocol layering
  The two objects under each layer at both sites should be identical
  If we want bidirectional communication, we need to make each layer so that it can perform two opposite tasks, one in each direction
    Transmitter (Tx)
    Receiver (Rx)

## Slide 28: Data Communications N Layering
Layer N
[Layer N-1 PDU]
Service Data Unit (SDU)
Layer N PDU
At each level N, two entities at the communicating devices (layer N peers) exchange protocol data units (PDUs) by means of a layer N protocol
Layer N
[Layer N+1 PDU]
Service Data Unit (SDU)
Each PDU contains a payload, called the service data unit (SDU), along with protocol-related headers or footers.
Layer N-1
[Layer N PDU]
Service Data Unit (SDU)
[Layer N PDU]
Service Data Unit (SDU)
Layer N-1 PDU
Layer N-1

## Slide 29: Data Communications Layering : Sending a letter (example)
SDU : the letter
PDU : the envelop with the receiver & the sender information
  Protocol related header (Names, addresses, postcodes)
Layer N : the sender, the receiver
  Both can send letters and receive envelopes
Layer N protocol : rules for writing the information of the receiver and the sender to the envelope
Layer N-1 : postbox and mailbox
  They are not bidirectional!!!

## Slide 30: ISO OSI 7 Layer Reference Model

## Slide 31: Data Communications ISO OSI reference model (7 layers)

## Slide 32: Data Communications Seven layers and Networking protocols
Data
Communications
Computer
Networks
Application dependent,
Presentation
(Network
Security)

## Slide 33: Data Communications ISO OSI reference model (7 layers)
Identifiers
  Each layer defines two kinds of identifiers
    Entity (Object) Identifier
      Unique Identifier to distinguish the peer object within the Layer
      (IETF) Internet Address (IPv4 and IPv6 addresses)
    Identifier for Multiplexing (Service Access Point (SAP) Identifiers)
      (Usually unique) Identifier to distinguish the object at the upper layer
      LLC Protocol Discrimination (LPD),
        IEEE 802 (and/or ISO/IEC) defines.
        0xAA/0xAB : SNAP (Subnetwork Access Protocol)
      Ethertype Protocol Discrimination (EPD)
        Ethertype (IETF)
        0x0800 (Internet Protocol Version 4)

## Slide 34: Data Communications ISO OSI reference model (7 layers)
Examples
  Application Layer
    Identifier
      Uniform Resource Locator (URL): http://www.korea.ac.kr/mbshome/mbs/university/index.do
      Telephone number: +82 2 3290 1234
    Identifier for multiplexing: N/A
  Transport Layer
    TCP (Protocol ID)
      Identifier
        Connection identifier <local endpoint, peer endpoint>
        Socket identifier : mapping table <local endpoint, peer endpoint>socket id
      Identifier for multiplexing : Well-known port number (0x0080,0x8080)
        https://www.iana.org/assignments/service-names-port-numbers/service-names-port-numbers.txt
    UDP (Protocol ID)
      Identifier
        Local endpoint
        Socket identifier : mapping table <local endpoint>socket id
      Identifier for multiplexing : Well-known port number

## Slide 35: Data Communications ISO OSI reference model (7 layers)
Examples
  IP (IPv4/IPv6)
    Identifier
      Address Family (AF_INET, AF_INET6)
      IP address (IPv4 address, IPv6 Address)
      Individual address (Unicast address) and Group address (multicast address)
    Identifier for multiplexing : protocol number
      https://www.iana.org/assignments/protocol-numbers/protocol-numbers.xhtml
  IEEE 802.3/11/15.4 (Ethernet, WLAN, WSN)
    Identifier
      Extended Unique Identifier (EUI-48); MAC-48
      Extended Unique Identifier (EUI-64)
    Identifier for multiplexing :
      Ethertype (2octets) : IEEE 802.3 Ethernet Frame
      LLC Address (1octet): IEEE 802.11 with SNMP (Protocol Identifier (5octets): OUI (3octets)+Ethertype(2octets))
      https://www.iana.org/assignments/ieee-802-numbers/ieee-802-numbers.xhtml

## Slide 36: Data Communications Physical layer
The physical layer defines the electrical and physical specifications of the data connection.
It defines the relationship between a device and a physical transmission medium
  the layout of pins, voltages, line impedance, cable specifications, signal timing
  similar characteristics for connected devices and frequency (5 GHz or 2.4 GHz etc.) for wireless devices.

## Slide 37: Data Communications Physical layer
It may define transmission mode as simplex, half duplex, and full duplex.
It defines the network topology as bus, ring, or star being some of the most common.

## Slide 38: Data Communications Ethernet Physical layers names
10, 100, 1000, 10G
  the nominal, usable speed at the top of the physical layer
BASE, BROAD, PASS
  baseband, broadband, or passband signaling
-T, -S, -L, -C, -K, -F...
  medium
    T = twisted pair,
    F = fiber, various wavelengths
    S = 850 nm short wavelength (multi-mode fiber),
    L = 1300 nm long wavelength (mostly single-mode fiber)
X, R
  PCS encoding method (varying with the generation)
    X for 8b/10b block encoding (4B5B for Fast Ethernet),
    R for large block encoding (64b/66b)
1, 2, 4, 10
  LAN PHYs: number of lanes used per link
Baseband
near-zero frequency range
Broadband
the wide range of frequencies
Passband
the range of frequencies or wavelengths that can pass through a filter
PCS (Physical Coding Sublayer)

## Slide 39: Data Communications Physical layer : Ethernet Example
100BASE-TX
  4B5B MLT-3 coded signaling
    MLT-3 = { +1V, 0V, -1V }
  Category 5 cable copper cabling with two twisted pairs
    The 8P8C (8 position 8 contact) modular connector
      RJ45 after a telephone industry standard
    Connectors are frequently terminated using the T568A or T568B assignments that are defined in TIA/EIA-568

## Slide 40: Data Communications Physical layer : Ethernet Example

## Slide 41: Data Communications Physical layer : Transmission Model

## Slide 42: Data Communications Physical layer : network topology
BUS
RING
STAR

## Slide 43: Data Communications Data Link Layer
The data link layer provides node-to-node data transfer using a link between two nodes which are directly connected to the link.
  The link is a conceptual link.
    It can be a physical medium.
    It can be a logical link established by using more complex protocols

## Slide 44: Data Communications Standards for Physical / Data Link Layer
Standards for logical link
  High-Level Data Link Control (HDLC)
    (ISO 13239) a bit-oriented code-transparent data link layer protocol
  Point-to-point Protocol (PPP)
    (RFC1661) a data link layer communications protocol used to establish a direct connection between two nodes
    (RFC1662) PPP in HDLC-like Framing
  IP in IP Tunneling (or IP Encapsulation within IP)
    (rfc1853) IP in IP Tunneling
    (RFC2003) IP Encapsulation within IP
  STP (Signal Transfer Point)
    (3GPP TS 29.016 V4.1.0 (2002-06))

## Slide 45: Data Communications Data Link Layer
The link at the data link layer must define frames for control, management, and data transfer between two nodes which are connected to the link
  It defines the protocol to establish and terminate a connection between two physically connected devices.
  It detects and possibly corrects errors that may occur during transferring frames using the link.
  It also defines the protocol for flow control between them

## Slide 46: Data Communications Standards for Physical / Data Link Layer
IEEE 802.3 ETHERNET
  802.3
    1G/5G/10G/25G/100G/400G
  802.3bp-2016 1000BASE-T1
    Gigabit Ethernet over a single twisted pair, automotive & industrial environments
IEEE 802.11 Wireless LAN
  802.11
    2M/11M(11b)/54M(11g)-2.4Ghz-20Mhz
    54M(11a)-5GHz-20Mhz
    150M(11n)-2.4/5GHz-40Mhz
    866M(11ac)-2.4/5Ghz-160Mhz (single Spatial stream) (WiFi5)
    1.2G(11ax)-2.4/5GHz-160Mhz- ((single Spatial stream) 6Extension- higher than 6Ghz
    6.7G(11ad)-60GHz-2160Mhz
  802.11p for VANET (WAVE:US & C-ITS: Europe)
    5.85-5.925 GHz-10MHz x 7 channels
  802.11ah for IoT (radius: up to 1km)
    800Mhz (Europe) or 900Mhz (USA), 1-16Mhz, 300kbps-86.7Mbps (single Spatial stream)
IEEE 802.15.4 Wireless Sensor Network (IoT)

## Slide 47: Data Communications Network Types
The criteria of distinguishing one type of network from another is difficult and sometimes confusing
  size,
  geographical coverage, and
  ownership

## Slide 48: Data Communications Network Types
A local area network (LAN) is usually owned by the same organization that owns attached devices
  Smaller scope, typically a single building
  Internal data rates greater than WANs
Most common configurations are switched LANs and wireless LANs

## Slide 49: Data Communications Network Types
A wide area network (WAN) has a wider geographical span, spanning a town, a state, a country, or even the world
  a WAN interconnects connecting devices such as switches, routers, or modems
  a WAN is normally created and run by communication companies and leased by an organization that uses it
    Requiring the crossing of public right-of-ways

## Slide 50: Data Communications Network Types
A Metropolitan Area Network (MAN) provides a middle ground between LANs and WANs, typically spanning a town, city, suburb or metro area with higher speed connections
  Private or public network

## Slide 51: IEEE 802 Reference Model
Informational
Nested Layering - Sublayers

## Slide 52: Physical Layer IEEE 802-2014 Reference models

## Slide 53: Physical Layer IEEE 802-2014 Reference models
IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture
DLL data link layer
PHY physical layer (OSI reference model and IEEE 802® RM)
LSAP link service access point
MSAP MAC service access point
PSAP physical service access point
MIB management information base
MICF media-independent control function
MICLSAP media-independent control link service access point
MICPSAP media-independent control physical service access point
MICSAP media-independent control service access point
MIH media-independent handover
MIHF media-independent handover function

## Slide 54: Physical Layer IEEE 802.3 Ethernet Example
IEEE Std 802.3-2008 CSMA/CD

## Slide 55: Physical Layer IEEE 802.3 Ethernet Example
IEEE Std 802-2014 OVERVIEW AND ARCHITECTURE
an example of an end-station implementation model (UM) (100 Gb/s)

## Slide 56: Physical Layer IEEE 802.11-2020 WLAN Example
IEEE Std 802.11-2012 WIRELESS LAN MAC AND PHY SPECIFICATIONS