## Slide 1: Data Link Layer HDLC and IEEE Frames
Lecture 01

## Slide 2: Content
High-level Data Link Control (HDLC)
  The reference model of data link layer protocols
Data Link Layer Standards
  ISO/IEC 8802-2 (IEEE 802.2 obsoleted)
    Logical Link Control Sublayer
  IEEE 802-2014
    IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture

## Slide 3: Data Link Layer Data Link Layer fundamental functions
Frame
  The unit of data to be sent by a DLL protocol
Addressing
  Identifying an entity on the DLL network
Data transfer
Media Access Control
  Controlling the transmission of the frames
Flow control
  Controlling the transmission speed of a sender
Error control
  Detecting and correcting transmission errors
Management
  Maintaining the data link layer

## Slide 4: Data Link Layer Protocols
High-level Data Link Control (HDLC) the reference model of data link layer protocols

## Slide 5: Data Link Layer Protocols High-level Data Link Control (HDLC)
The HDLC is based on IBM's Synchronous Data Link Control (SDLC) protocol, which is the layer 2 protocol for IBM's Systems Network Architecture (SNA).
Synchronous Data Link Control (SDLC) was originally designed to connect one computer with multiple peripherals

## Slide 6: Data Link Layer Protocols High-level Data Link Control (HDLC)
A bit-oriented code-transparent synchronous data link layer protocol developed by ISO
  The original standards for HDLC
    ISO 3309 – Frame Structure
    ISO 4335 – Elements of Procedure
    ISO 6159 – Unbalanced Classes of Procedure
    ISO 6256 – Balanced Classes of Procedure
  The current standard for HDLC is ISO 13239

## Slide 7: Data Link Layer Protocols High-level Data Link Control (HDLC)
HDLC services
  Connection-oriented service
    (Reliable) in-sequence frame delivery
      Flow Control
        Controlling the sender’s Tx speed by the receiver
        (point-to-multipoint) in turn
        (point-to-point) flow control
      Error Control
        Frames with errored bits: FCS (CRC)
        Lost frames: Frame sequence and retransmission timer
  Connectionless service
    No guarantee for the frame delivery

## Slide 8: Data Link Layer Protocols High-level Data Link Control (HDLC)
HDLC operation mode
  (point to multipoint connections)
    Master-slave mode
      Normal Response Mode (NRM)
      Asynchronous Response Mode (ARM)
  (point-to-point mode)
    Peer-to-peer mode
      Asynchronous Balanced Mode (ABM)

## Slide 9: Data Link Layer Protocols HDLC Operation Mode
Receiver/Sender
Receiver
Sender
NRM/NRME (normal response extended mode)
ARM/ARME (asynchronous response extended mode)
ABM/ABME (asynchronous balanced extended mode)
Balanced, which consists of two peer terminals.
Extended mode : 7-bit sequence number in the control field
Unbalanced, which consists of one primary terminal, and one or more secondary terminals.

## Slide 10: Data Link Layer Protocols HDLC Operation Mode
Normal Response Mode (NRM)
  The computer gives each peripheral permission to speak in turn
  Commands and responses are indistinguishable
    The only difference is the direction in which they are transmitted
  Normal response mode allows operation over half-duplex communication links

## Slide 11: Data Link Layer Protocols HDLC Operation Mode
Asynchronous Response Mode (ARM)
  Master-slave mode
  It allows operation over full-duplex communication links
    It allows the slave computer to transmit at any time

## Slide 12: Data Link Layer Protocols HDLC Operation Mode
Asynchronous balanced mode (ABM)
  The concept of a combined terminal which can act as both a primary and a secondary.
  The address field of a received frame must be examined to determine [whether it contains a command or a response].
    If the address = mine, command
    Otherwise, response

## Slide 13: Data Link Layer Protocols HDLC Frame structure
Flag : Start/end frame delimiter (0x7E)
Address
Command : receiver’s address, Response: the sender’s address
Control
HDLC control information including frame type
8 bits : normal mode (use 3-bit sequence number)
16 bits: extended mode (use 7-bit sequence number)
FCS (Frame Check Sequence)
16 bits : CRC-CCITT;
32 bits : CRC-32;

## Slide 14: Data Link Layer Protocols HDLC Framing
HDLC frames can be transmitted over synchronous or asynchronous serial communication links.
  ‘0x7E’ is used to delimiter frames
  Synchronous serial communication link
    Sending empty frames even if there is no data available to be sent
  Asynchronous serial communication link
    No frame is sent if there is no data available to be sent

## Slide 15: Data Link Layer Protocols HDLC Framing: Synchronous link
When no frames are being transmitted on a simplex or full-duplex synchronous link, a frame delimiter (0x7E) is continuously transmitted on the link

## Slide 16: Data Link Layer Protocols HDLC Framing
Escaping control characters in user data
  "control-octet transparency“
  Synchronous framing: bit stuffing
    Any time that 5 consecutive 1-bits appear in the transmitted data, the data is paused and a 0-bit is transmitted
    (sender) 0111 1110 0111 1101 0 (receiver) 0111 1101 0 0111 1110
  Asynchronous framing: byte/octet stuffing
    "control escape octet“ : '01111101', (0x7D)
    If either of 0x7E/0x7D appears in the transmitted data, an escape octet is sent, followed by the original data octet with bit 5 (7..0) inverted
      Example : "01111110“ (0x7E) would be transmitted as "01111101 01011110" (0x7D 0x5E)

## Slide 17: Data Link Layer Protocols HDLC Framing: Bit Stuffing

## Slide 18: Data Link Layer Protocols HDLC Framing: Byte Stuffing

## Slide 19: Data Link Layer Protocols HDLC Frame Types
Information frames (or I-frames)
  User Information frame for connection-oriented service
Supervisory Frames(or S-frames)
  Control frame for flow and error control
  It is used whenever piggybacking the control information is impossible or inappropriate.
Unnumbered frames(or U-frames)
  Various miscellaneous purposes
    Link management frame
    User Information frame (UI frame) for connectionless service

## Slide 20: Data Link Layer Protocols HDLC Frame Types
Common frame types at the data link layer
  Control Frame
    Controlling data frame transfer
    HDLC: Supervisory Frames (they can be piggybacked at the I-frames)
  Data Frame
    Containing user date to be transferred.
    HDLC: Information frames or UI (Unnumbered Information) frame
  Management Frame
    Maintaining a connection (or an association) between peer nodes
      Establishing/tearing down a connection
      Negotiating optional configurations or functions between peer nodes
    HDLC: Unnumbered frames except UI frames

## Slide 21: Data Link Layer Protocols HDLC Control Field
Contents of the HDLC Control Field depend on a frame type.
  Supervisory Frames
    The status of the data frame delivery operation
  Information frames
    I-frames: the current data position for the sending data stream (connection-oriented).
      If an S-frame is piggybacked, the current data position of the received data stream
    UI-frame: no status information (connectionless)
  Management Frame
    The type of Management frames

## Slide 22: Data Link Layer Protocols HDLC Control Field
LSB
LSB
Transmission direction: LSB (bit0) first
The P/F bit
Poll/Final is a single bit with two names.
  Poll (command) : when set by the primary station to obtain a response from a secondary station
  Final (response) : when set by the secondary station to indicate a response or the end of transmission.
In all other cases, the bit is clear.

## Slide 23: Data Link Layer Protocols HDLC Control Field
The P/F bit
  The bit is used as a token [that is passed back and forth between the stations].
    The primary station sets the POLL to obtain a response from a secondary station
    The secondary station only sets the FINAL to indicate the end of transmission.
  Only one token should exist at a time.
    The primary only sends a Poll when it has received a Final back from the secondary, or after a timeout indicating that the bit has been lost

## Slide 24: Data Link Layer Protocols HDLC Connection Management (U-Frame)
A connection initialization can be requested by either side
  A station sends a ‘set’ (U-frame) specifying the operation mode to the other side
    (NRM, ARM, ABM)
      Specifies 3-bit sequence numbers are in use
    NRME, ARME, ABME (Extended mode)
      Specifies 7-bit sequence numbers are in use
  The other responses with ‘Unnumbered Acknowledgement’ (UA; U-frame)

## Slide 25: Data Link Layer Protocols HDLC Connection Management (U-Frame)
Connection initialization/termination

## Slide 26: Data Link Layer Protocols HDLC Connection Establishment and termination

## Slide 27: Data Link Layer Protocols HDLC S-frame
Connection oriented service : User data
S-Frame: (bit1..bit0:[01])
S-frame subtype: (bit3..bit2) – used for Flow Control and Error Control
  RR(00): the frame N(R) is expected (N(R)-1 is received), and the sender may send new frame
  RNR(01): the frame N(R) is expected (N(R)-1 is received), but the sender is prohibited to send new frame until new S-frame with (RR) is arrived.
  REJ(10): the frame N(R) is in error (corrupted or lost): see flow-control ppt
    the sender retransmits frames from N(R) to the last transmitted frame
  SREJ(11): the frame N(R) is in error (corrupted or lost): see flow-control ppt
    the sender retransmits the frame N(R)

## Slide 28: Data Link Layer Protocols HDLC I-frame
Connection oriented service : User data
I-Frame
It is used to transfer user information of a connection-oriented service
N(R): the frame N(R) is expected from the other side.
  Eliminating a S-frame with RR (N(R))
N(S): the sequence number of the transmitting frame

## Slide 29: Data Link Layer Protocols HDLC UI-frame
UI-frame
  (U-frame (bit1..bits0(11)); subtype(bit7..bit5, bit3..bit2(000 00)): Information)
  It is used to transfer user information for connectionless service
  The connectionless service does not need the P/F field, the sequence number field as well as S-frame.
    C-Field (bit7..bit1(0000 0011; 0x03)

## Slide 30: Data Link Layer Standards
IEEE 802-2014
ISO/IEC 8802-2 (IEEE 802.2 obsoleted)

## Slide 31: IEEE 802-2014 Data Link and Physical Layers
IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture

## Slide 32: IEEE 802-2014 Current family of IEEE 802 standards

## Slide 33: Data Link Layer Standards
IEEE 802-2014
  Overview and Architecture
ISO/IEC 8802-2 (IEEE 802.2)
  Logical Link Control
IEEE 802.1AC-2016 (the Internal Sublayer Services)
  Medium Independent Access Control(MAC) - ISS
IEEE 802.3-2022 Ethernet
  Medium Access Control for Ethernet
IEEE 802.11-2020 WLAN
  Medium Access Control for Wireless Medium

## Slide 34: Physical Layer IEEE 802-2014 Reference models
IEEE Std 802-2014 OVERVIEW AND ARCHITECTURE
IEEE 802 Reference Model (RM) for end stations

## Slide 35: IEEE 802-2014 Reference Model description for end stations
LLC sublayer in 802 Reference Model

## Slide 36: Data Link Layer Standards ISO/IEC 8802-2 (IEEE 802.2) logical link control
LSAP(Link Service Access Point) :
  The logical concatenation of the LLC address field and the MAC address field
  Identifiers for Upper layers
    LLC address field
    LLC address with SNAP (Subnetwork Access Protocol) (IEEE 802.11)
      LLC: 0xAAAA03; DSAP-SSAP-Control (0xAA/AB = SNAP identifier)
      SNAP: Protocol identifier (5octets);
        an OUI field (3octets:00-00-00) and an Ethertype field (2octets)
    Ethertype (IEEE 802.3)

## Slide 37: IEEE 802-2014 Reference Model description for end stations
Higher Layer Protocol Discrimination Entity (HLPDE)
  EtherType protocol discrimination (EPD)
    Ethertype
  LLC protocol discrimination (LPD)
    LLC address field
    LLC address with SNAP (Subnetwork Access Protocol)
  Each IEEE 802 standard describes the HLPDE.

## Slide 38: Data Link Layer IEEE 802-2014
IEEE 802 networks use frame-based communications over a variety of media to connect various digital apparatus regardless of computer technology and data type
The basic communications capabilities provided by all IEEE 802 standards are frame based with source and destination addressing and asynchronous timing (no common clock)
In a frame-based system, the format is a variable-length sequence of data octets.
Apparatus [명사] 기구, 장치

## Slide 39: IEEE 802-2014 Reference Model description for end stations
The MAC sublayer performs the functions necessary to provide frame-based, connectionless-mode‌ data transfer between stations in support of the LLC sublayer for networks that support it

## Slide 40: IEEE 802-2014 Reference Model description for end stations
The principal functions of the MAC sublayer
  Frame delimiting and recognition
  Addressing of destination stations (both as individual stations and as groups of stations)
  Conveyance of source-station addressing information
  Transparent data transfer of PDUs from the next higher sublayer
  Protection against errors, generally by means of generating and checking frame check sequences
  Control of access to the physical transmission medium

## Slide 41: IEEE 802-2014 Reference Model description for end stations
MAC entities use their respective PHY entities to exchange bits with their peers.
The PHY provides the capability to transmit and receive modulated signals assigned to specific frequency channels for broadband or wireless media or to a single baseband-channel.

## Slide 42: IEEE 802-2014 Reference Model description for end stations
The PHY service offered to the MAC sublayer is expressed as the transfer of bits (in sequences representing MAC frames)
The symbols [that are encoded for transmission] do not always represent individual bits.
  Symbol:
    It is the basic unit of transmitted modulated signal at the PHY.
    It usually contains several data bits.

## Slide 43: Common Interconnection and interworking with several links or networks
PHY interconnection
  Repeaters: extending the distance of a link by connection two segment links.
MAC interconnection
  Bridges: extending the coverage of a local area network
Network-layer inter-networking
  Routers: extending the coverage of a network layer consisting of several networks.

## Slide 44: IEEE 802-2014 MAC-sublayer interconnection: Bridges
Internal organization of the MAC sublayer with bridging

## Slide 45: Data Link Layer Standards
ISO/IEC 8802-2 Logical Link Control

## Slide 46: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
The ISO/IEC 8802-2:1998 standard
  define Logical Link Control (LLC) as the upper portion of the data link layer of the OSI Model
The LLC provides a uniform interface to the user of the data link service, usually the network layer.

## Slide 47: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
This International Standard describes the functions, features, protocol, and services of the Logical Link Control (LLC) sublayer in the ISO/IEC 8802 LAN Protocol
  The LLC sublayer constitutes the top sublayer in the data link layer
  It is common to the various medium access methods (MAC) that are defined and supported by the ISO/IEC 8802 activity

## Slide 48: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control

## Slide 49: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
Service primitives
Time-sequence diagrams

## Slide 50: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
Three forms of service
  Unacknowledged connectionless-mode services
  Connection-mode services
  Acknowledged connectionless-mode services

## Slide 51: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
Unacknowledged connectionless-mode services
  This set of data transfer services provides the means by which network entities can exchange link service data units (LSDUs) without the establishment of a data link level connection.
  The data transfer can be point-to-point, multicast, or broadcast

## Slide 52: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
Connection-mode services
  This set of services provides the means for establishing, using, resetting, and terminating data link layer connections
  These connections are point-to-point connections between LSAPs.

## Slide 53: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
Connection-mode services
  connection establishment service
  connection termination service
  connection reset service
  connection-oriented data transfer service
    This service also provides data link layer sequencing, flow control, and error recovery
  connection flow control service

## Slide 54: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
Acknowledged connectionless-mode services
  The acknowledged connectionless-mode data unit exchange services provide the means by which network layer entities can exchange link service data units (LSDUs) that are acknowledged at the LLC sublayer, without the establishment of a data link connection.
  The data unit transfer is point-to-point

## Slide 55: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
Data Transfer Primitives for Network Layer
  Unacknowledged connectionless-mode data transfer
    DL-UNITDATA.request
    DL-UNITDATA.indication
  Connection-mode data transfer
    DL-DATA.request
    DL-DATA.indication
  Acknowledged connectionless-mode data transfer
    DL-DATA-ACK.request
    DL-DATA-ACK.indication
    DL-DATA-ACK-STATUS.indication

## Slide 56: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
DL-UNITDATA.request/indication parameters
  source_address
    the local LSAP
      LSAP(Link Service Access Point) : the logical concatenation of the MAC address field and the LLC address field
  destination_address
    the remote LSAP
    either an individual or group address
  Data
    the link service data unit to be transferred by the data link layer entity
  Priority
    the priority desired for the data unit transfer

## Slide 57: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
Primitives for the MAC sublayer
  MA-UNITDATA.request
  MA-UNITDATA.indication
  MA-UNITDATA-STATUS.indication

## Slide 58: Data Link Layer Standards ISO/IEC 8802-2 Logical Link Control
MA-UNITDATA.request/indication
  source_address
    an individual MAC sublayer entity address
  destination_address
    either an individual or a group MAC sublayer entity address
  routing_information
    the route desired for the data unit transfer (source-routing only – token ring)
  Data
  Priority
  service_class
    the class of service desired for the data unit transfer

## Slide 59: Data Link Layer Standards IEEE 802.1AC-2016
IEEE 802.1AC-2016
  Media Access Control (MAC) Service Definition
  It defines the Internal Sublayer Services
  It also defines mapping parameters between the ISS MSAP and the MSAP of each media dependent standards (IEEE 802.3, IEEE 802.11, etc).
The MAC service definition was first standardized as ISO/IEC 15802-1:1995

## Slide 60: Data Link Layer Standards ISO/IEC 8802-2 LLC Protocol Data Unit (PDU)

## Slide 61: Data Link Layer Standards ISO/IEC 8802-2 LLC PDU LLC address field
DSAP | SSAP=0xAAAA
10101010 10101010
I/G=(0)Individual DSAP
C/R=(0)Command

## Slide 62: Data Link Layer Standards ISO/IEC 8802-2 LLC PDU LLC Control field

## Slide 63: Data Link Layer Standards MAC Sublayer Standards
IEEE 802.3 and IEEE 802.11 MAC frames

## Slide 64: MAC Sublayer Standards MAC sublayers : Wired and Wireless LAN

## Slide 65: MAC Sublayer Standards 802.3-2022 Ethernet 3.1.1 Packet format
46 : minFrameSize (64 octets) – (DA+SA+Length/Type+FCS)
1500 decimal—basic frames
1504 decimal—Q-tagged frames
1982 decimal—envelope frames
Figure 3–1—Packet format

## Slide 66: MAC Sublayer Standards 802.3-2022 Ethernet 3.1.2 Service interface mappings
Figure 3–2—Service primitive mappings

## Slide 67: MAC Sublayer Standards 802.11-2020 WLAN
Genera MAC frame format

## Slide 68: The summary of DLL/MAC frames HDLC, 802.3/Ethernet, 802.11
Address
DA
SA
SDU
PPP[Protocol/SDU]
SDU
FCS
FCS
A1
A2
A3
A4
SDU
FCS
Control
(Length)/Type
PAD
FC
Duration
Sequence
Control
QoS
Control
HT
Control
HDLC | IEEE 802.3 frame | IEEE 802.11 frame
I-frame | N/A (only connectionless) | N/A
S-frame | N/A (no flow control & error correction) | Control frame (no flow control)
U-frame | Management frame | Management frame (N/A)
UI-frame | MAC frame | Data frames
Control Field: Frame Type(bit0 or bit[1..0]) | N/A | Type subfield of Frame Control field (Type bit[3..2])
Control Field: Frame sequence | N/A | Sequence Control
Control Field: Poll/Final | N/A | Control frame (QoS +Poll)
Upper Layer Identifier: Not in HDLC (Protocol field of PPP frame) | Ethertype | LLC/SNAP (Ehthertype)
Peer entity address: address field (DA or SA) | DA field (and SA field for a response frame) | DA field (and SA field for a response frame)
DSAP
SSAP
CTL
SNAP
[000000/Type]
SDU
LLC Frame (802.2 Frame )
MAC Frame