## Slide 1: Data Link Layer (DLL) Flow control Error Control
LECTURE 03

## Slide 2: Content
Reliable Communication
Flow Control
  Stop-and-Wait
  Sliding Window
Error Control
  Error Detection
    Cyclic redundancy checks (CRC)
  Error Correction/Recovery
    Automatic Repeat request (ARQ)

## Slide 3: Data Link Layer Functions
Frame
  The unit of data to be sent by a DLL protocol
Addressing
  Identifying an entity on the DLL network
Data transfer
Medium access control
  Accessing the physical medium to transmit frames
Flow control
  Controlling the transmission speed of a sender
Error control
  Detecting and correcting transmission errors
Management
  Maintaining the data link layer

## Slide 4: Reliable Communication
Flow Control and Error Control

## Slide 5: Data Link Layer Reliable Communication
Reliability
  Delivering frames without errors
  In-sequence delivery of frames without duplicated frames

## Slide 6: Data Link Layer Reliable Communication
Frame Errors during frame transportation
  Frames can be lost during transportation
  Data in the frame are corrupted (Bit errors in the frame).
Solutions for frame errors
  Detecting a lost or corrupted frame
    It should use the cyclic redundancy check (CRC) to detect errored bits in a frame.
    It should use a kind of sequence numbers to detect lost frames in a connection.
  Recovering a lost or corrupted frame
    It may use retransmission of lost or corrupted frame, but it causes out-of-order frames. and duplicated frames.
    It may use a forward error correction (FEC) code to correct errors in the corrupted frame at the destination, but it requires redundancy in the frame.

## Slide 7: Data Link Layer Reliable Communication
Frame lost at the destination station
  Resource in the destination node of frames is not sufficient
    Buffer Overflow
  Resources in the intermediate nodes of the path [through which frames pass] are not sufficient.
Solutions for frame lost due to lack of resource (Queue Size)
  Too many frames at the destination node of frames in a connection
    Control the speed of sending frame at the source node (Flow control)
  Too many frames at the intermediate nodes
    Drop some frames randomly (RED) or drop the latest frame arrived at the nodes (Tail Drop).

## Slide 8: Flow Control
It assume that there is no error during frame exchange

## Slide 9: Data Link Layer (DLL) Flow Control
Flow control is the process of managing the rate (or amount) of data transmission between two nodes to prevent a fast sender from overwhelming a slow receiver
Typically, the receiver controls the sender.
Assumption
  Error-free situation.

## Slide 10: Data Link Layer Flow Control
Flow control operates on a connection-oriented service
  A point-to-point connection
  Acknowledged Connectionless service

## Slide 11: Data Link Layer Flow Control
Flow control strategy
  Stop-and-wait
    The sender may send at most one frame
  Sliding Window (amount of data (N) to be sent without any acknowledgement from the receiver)
    The sender may send at most N frames
      The window size: N
  Rate Control (speed of transmission to be used)
    The sender may send at most R Mbps
      binary indication : increase/decrease the current speed (+/-)
      absolute rate

## Slide 12: Data Link Layer Flow Control
Flow Control is done independently for each directions.
  Peer A/B (TX, RX): a bidirectional connection
    Peer A (TX) : the sender (N(S)) → the receiver Peer B (N(R))
    Peer B (TX) : the sender (N(S’)) → the receiver Peer A (N(R’))
  There is a sequence number for each direction.
    Peer A/B have a pair of (N(S) and N(R)), and
    N(S) and N(S’) are independent each other.

## Slide 13: Data Link Layer Flow Control: Stop-and-wait
Stop-and-wait
  A sender waits the acknowledgement (ACK) of a frame from a receiver after it sent the frame to the receiver
    The sender can send only a single frame and must wait the ACK of the frame
Remember the flow control assumption
    Error-free: The frame and its ACK are never lost or corrupted

## Slide 14: Data Link Layer Flow Control: Stop-and-wait
HDLC (1): Stop-and-wait
  P/F subfield at the control field
    The P/F bit is used as a token [that is passed back and forth between the stations].
    Only one token should exist at a time.
      The primary only sends a Poll when it has received a Final back from the secondary, or after a timeout indicating that the bit has been lost

## Slide 15: Data Link Layer Flow Control: Stop-and-wait
HDLC (2): Stop-and-wait
  The sender waits the acknowledgement (ACK) of the latest frame that it sent.
    The sender may send a next frame (N(S)+1) when it receives the ACK (N(R)=N(S)+1) of the frame
    HDLC:
      (S-FRAME) A Receiver Ready (RR) with N(R) or
      An I-Frame with N(R)

## Slide 16: Data Link Layer Flow Control: Sliding Window
Sliding Window (Window-based)
  Window Size : the number of frames can be sent without receiving ACKs
    The new window size [to update the current window size] can be explicitly/Implicitly carried in an Acknowledgement
    The window size is initialized (or negotiated) during the connection establishment.
    It can be fixed or be varying during the connection lifetime.

## Slide 17: Data Link Layer Flow Control: Sliding Window
Window Size
  HDLC (Data Link Layer Protocol)
    Fixed window size is chosen during the connection establishment
      Sequence Number Range: 3bits or 7bits (extended)
    (Implicit) Window size is incremented by one whenever an ACK is arrived at the sender
  Transport or Application Protocol
    Window Size is initialized by the receiver during the connection establishment
    (Explicit) The receiver includes the window size (WIN (offset)) in acknowledgements.
      Maximum sequence number to be sent = ACK (N(R))+WIN

## Slide 18: Data Link Layer Flow Control: Sliding Window
HDLC Window Size
  The window size is determined by the HDLC operation mode and Error recovery method (ARQ).
    HDLC operation mode: Sequence number (SN) Range
      ; The number of bits (n) for the sequence number field
      Normal mode (3-bit sequence number): 8 ()
      Extended mode (7 bits sequence number): 128 ()
    HDLC Error recovery:
      determines the maximum window size (N)
      Go-back-N (ARQ) : SN-1; 7 or 127
      Selective repeat ARQ: ; 4 or 64

## Slide 19: Data Link Layer Flow Control
IEEE 802.3 Ethernet – wired medium (low error rate)
  Only unacknowledged connectionless service
  No flow control is supported
    No control field for flow control
IEEE 802.11 WLAN –wireless medium (high error rate)
  Acknowledged connectionless service
  Sliding Window
    The number of bits (16 bits) for sequence control field
      Sequence Number field (12 bits)
      Fragment Number field (4 bits)

## Slide 20: Data Link Layer Error Control

## Slide 21: Data Link Layer Error Control
Error Control
  Error detection
  Error Correction (or Error Recovery)

## Slide 22: Data Link Layer Error Control
The general idea for achieving error detection
  Sender
    Adding some redundancy to a message
  Receiver :
    Checking consistency of the delivered message using the redundancy in the frame.

## Slide 23: Data Link Layer Error Control
The general idea for achieving error recoveries
  Recovering data that has been determined to be corrupted or lost.
    Ignoring corrupted or lost frames.
      An upper layer protocol handles this case.
    Retransmission of corrupted or lost frames (Backward Error Correction)
      A feedback (Negative ACK (NACK)) is required from the receiver to the sender.
      The feedback usually includes the information for the errored or lost frames.
    Adding more redundancy (Forward Error Correction (FEC)) to be able to correct the corrupted frame at the receiver.
      It still requires a method for lost frames.
      Added redundancy is quite large.
        To reduce the amount of redundancy, FECs are usually coupled with picturing (omitting some predefined-position bits from the input data)

## Slide 24: Data Link Layer Error Control
Backward Error Correction
  An error detection scheme is combined with requests for retransmission of corrupted frames
    Automatic Repeat reQuest (ARQ)
  Data Link layer and above
Forward Error Correction (FEC)
  The sender encodes data using an error-correcting code (ECC) prior to transmission.
  The redundancy (added by the code) is used by the receiver to recover the original data.
  Physical Layer: Wireless links or high speed wired links.

## Slide 25: Data Link Layer Error Detection Schemes
Cyclic Redundancy Checks (CRC)

## Slide 26: Data Link Layer Error detection schemes
Error detection is most commonly realized using a suitable hash function (or checksum algorithm).
  A hash function adds a fixed-length tag to a message.
  Receivers verify the delivered message by recomputing the tag and comparing it with the one in the message.

## Slide 27: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
A non-secure hash function designed to detect accidental changes to digital data in computer networks.
Binary division
  Finite Algebra Theory (Galois Fields)
    The divisor
      a generator polynomial
    The dividend
      the input data
    The remainder (tag; redundancy)
    The result of (polynomial long) division

## Slide 28: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
Let us assume k message bits and r bits of redundancy
  kkkkkkk rrrr:
  block length n = k+r
Let bits in the message associate with coefficients of a polynomial:

## Slide 29: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
Let M(x) be the message polynomial
Let G(x) be the generator polynomial
  G(x) is fixed for a given CRC scheme (defined in the standard)
  G(x) is known both by sender and receiver
Create a block polynomial F(x) based on M(x) and G(x) such that F(x) is divisible by G(x)

## Slide 30: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
A Sender:
  Multiply M(x) by br: (if b=2, M(x)≪r)
  Divide M(x)br by G(x): +C(x)
  Ignore the quotient and keep the reminder C(x)
  Form F(x) = M(x)br+C(x)
  Send F(x)
A Receiver:
  When it receives F’(x), divide F’(x) by G(x)
  Accept if the remainder is 0, reject otherwise

## Slide 31: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
  F(x) = M(x)br+C(x) =
    M(x)br =
In Binary modular addition (XOR)
  C(x) is the remainder of G(x), so M(x)br mod G(x) = C(x)
  C(x)+C(x) = 0
    Example : 10101010=0000

## Slide 32: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
Shifting 3 bits
(Multiplying )

## Slide 33: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
bit-wise operation

## Slide 34: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)

## Slide 35: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
Properties of CRC
  All single bit error if G(x) has two or more terms
  All double (2 bits) errors (Isolated Single Bit Errors)
  All odd number of bit errors if G(x) has the (x+1) factor
    G(X)=(x+1)H(x)
  All short burst errors (t ≤ r)
    t : burst bit error length
  Long Burst Errors
    (t = r+1): Probability of not detecting the error:
    (t > r+1): Probability of not detecting the error is
See the following link for proofs:
  http://web.mit.edu/6.02/www/f2010/handouts/lectures/L7.pdf

## Slide 36: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
Generating Polynomials in standards
  CRC-12 = x12+x11+x3+x2+x+1
  CRC-16 = x16+x15+x2+1
  CRC-CCITT = x16+x12+x5+1
  CRC-16 and CRC-CCITT catch
    All single and double errors
    All odd number of bit errors
    All bursts of length 16 or less (t ≤ r=16)
    99.997% of 17-bit (t = r+1) error bursts
    99.998% of 18-bit (t > r+1) and longer error bursts
  CRC-32
    99.9999999767% of 34-bit (t > r+1) and longer error bursts
      missing one frame of more than one billion frames

## Slide 37: Data Link Layer Error detection schemes Cyclic Redundancy Checks (CRCs)
1011
Hardware design of the CRC divisor

## Slide 38: Data Link Layer Cyclic redundancy checks (CRCs)

## Slide 39: Data Link Layer CRC example
0
(0,0)=0
(0,1)=1
0
0
0
0
1
0
0
(0,0)=0
(0,1)=1
0
0
1
0
0
0
(0,0)=0
(0,0)=0
1
1
0
0
1
1
(1,1)=0
(1,0)=1
0
0
1
0
(0,0)=0
(0,0)=0
1
0
0
1
0
0
(1,0)=1
(1,0)=1
0
1
1
0
1
1
(0,0)=0
(0,1)=1
1
0
0
1
1
0

## Slide 40: Data Link Layer Error Recovery
Automatic Repeat reQeust (ARQ)

## Slide 41: Data Link Layer Error Recovery
Error control
  Error detection: control information
    Corrupted Frames
      (Trailer) Frame Check Sequence (FCS) field
        Cyclic Redundancy Check (CRC)
    Lost frames
      (Header) Frame Sequence Number field
  Error recovery (or correction)
    Drop
      drop the received frame, and do nothing
    Retransmission:
      Feedback information: Negative acknowledgement (error indication)
        Automatic Repeat reQuest (ARQ): HDLC S-frame (RR, REJ, SREJ)
      Retransmission Timer and Maximum number of retransmission

## Slide 42: Data Link Layer Error Recovery: DROP
Drop
  drop the received frame, and do nothing
Standard protocols with the drop policy
  IEEE 802.3 Ethernet
    FCS(CRC) & drop
  User Datagram Protocol (UDP):
    IP Checksum & drop

## Slide 43: Data Link Layer Error Recovery: Retransmission
Retransmission
  (1) The receiver notifies the corrupted or lost frames to the sender by sending negative acknowledgements (NACKs)
    NACKs include the sequence numbers of the corrupted or lost frames.
      An ACK includes the sequence number of the next expected frame.
      HDLC S-frame with REJ or SREJ used for a NACK.
    When the sender receives a NACK, then it re-transmits the notified frame.
  (2) The sender does not receive any ACK or NACK during a specified time period.
    After the expiry of the time period for a frame, the sender re-transmits the frame again until the predefined number of retransmission is performed.
The most well-know Retransmission Policy
  Automatic Repeat reQuest (ARQ)

## Slide 44: Data Link Layer Error Recovery: Retransmission
How does the sender know that a frame is delivered at the receiver?
  (a frame is arrived at the receiver)
    (the frame has no error)
      The receiver sends the positive acknowledgement (ACK) to the sender
        (The ACK is arrived at the sender)
          The sender knows that the frame is delivered at the receiver
        (The ACK itself is lost)
          The sender does not know whether the frame is delivered at the receiver.
          ( expired and ) The sender retransmits the frame to the receiver
            It causes that duplicated frames are received by the receiver.
    (the frame has errors)
      The receiver sends the negative acknowledgement (NACK) to the sender
        (The NACK is arrived at the sender)
          The sender knows the frame is not delivered at the receiver
          The sender retransmits the lost frame
        (The NACK itself is lost)
          The sender does not know whether the frame is delivered at the receiver.
          ( expired and ) The sender retransmits the frame to the receiver

## Slide 45: Data Link Layer Error Recovery: Retransmission
How does the sender know that a frame is delivered at the receiver?
  (a frame is not arrived at the receiver)
    (The next fame is arrived at the receiver)
      (flow-control: sliding window only)
      The receiver sends the NACK for the missing frame to the sender
        (The NACK is arrived at the sender)
          The sender knows the frame is not delivered at the receiver
          The sender retransmits the lost frame
            (Go Back N) Retransmitting all frames from the lost frame, or
            (Selective Repeat/Reject)) Retransmitting only the lost frame
        (The NACK itself is lost)
          The sender does not know whether the frame is delivered at the receiver
          ( expired and ) The sender retransmits the frame to the receiver
    (No frame to be sent is available at the sender)
      (flow-control)
        sliding window (window size is zero) or stop-and-wait
        sliding window (window size is not zero, but no frame in the buffer)
      The receiver does nothing.
        The sender does not know whether the frame is delivered at the receiver
        ( expired and ) The sender retransmits the frame to the receiver

## Slide 46: Data Link Layer Error Recovery Automatic Repeat reQuest (ARQ)
Automatic Repeat reQuest (ARQ)
  (Flow Control: Stop-and-wait)
    Stop-and-wait ARQ
  (Flow Control: Sliding Window)
    Go-Back-N ARQ
    Selective Repeat (Selective Reject) ARQ
Flow control and error control usually require feedbacks from the receiver, so both are implemented together.
  Flow control: Positive acknowledgement.
  Error control: Negative acknowledgement & Retransmission Timer

## Slide 47: Data Link Layer Error Recovery: ARQ Stop-and-Wait
FRAME
ACK
FRAME
ACK
FRAME
FRAME
FRAME
Duplicated FRAME
NACK
FRAME
NACK
FRAME
FRAME
FRAME
RTxTO
RTxTO
RTxTO
Next MSG
RTx FRAME
RTx FRAME
RTx FRAME
ACK
Lost ACK
FRAME
Corrupted Frame
FRAME
Lost Frame
FRAME
Filtering
duplicated frame

## Slide 48: Data Link Layer Error Recovery: ARQ Stop-and-Wait
Stop-and-Wait ARQ
  One bit sequence number (SN)
  Window size = 1
The sender needs a single frame buffer
Operation
  Initial values for sequence numbers of the peer A and peer B
    The sender role : (S)=0 at A; (S)=0 at B
    The receiver role : (R)=0 at B; (R)=0 at A
    Sequence number at the peer A: (S)=0, (R)=0
    Sequence number at the peer B: (S)=0, (R)=0

## Slide 49: Data Link Layer Error Recovery: ARQ Stop-and-Wait
0
1
0
0
1
0
1

## Slide 50: Data Link Layer Error Recovery: ARQ Go Back N
Sliding window
  n-bit sequence number
  Window size (W) :
    3-bit SN :
    7-bit SN :
The sender needs W frame buffers
The receiver needs only single frame buffer
Operation
  Initial value
    The sender : =W, (S)=0; (R)=0
    The receiver : (S)=0; (R)=0

## Slide 51: Data Link Layer Error Recovery: ARQ Go Back N
Frame 0
ACK 1
Frame 1
Frame 2
ACK 2
ACK 3
The total window size = W
The current window size =
0
0
1
1
2
n=2 (W=-1),
Accumulated Acknowledgement
Frame 0
Frame 1
Frame 3
ACK 0
so discard the frame
NACK 0
Frame 0
Frame 1
3
3
0
0
1
0
1
2
3
0
1
so accept the frame

## Slide 52: Data Link Layer Error Recovery: ARQ Go Back N
Frame 0
ACK 1
Frame 1
Frame 2
ACK 2
NACK 2
0
0
1
1
2
0
1
2
2
Frame 2
ACK 3
so discard the frame

## Slide 53: Data Link Layer Error Recovery: ARQ Go Back N: Window Size (

## Slide 54: Data Link Layer Error Recovery: ARQ Piggybacking S-frame in I-frame
0

## Slide 55: Data Link Layer Error Recovery: ARQ Selective Repeat (or Selective Reject)
Sliding window
  n-bit sequence number
  Window size (W) :
    3-bit SN :
    7-bit SN :
The sender needs frame buffers
The receiver needs frame buffers
Operation
  Initial value
    The sender: =W, (S)=0; (R)=0
    The receiver: (S)=0; (R)=0

## Slide 56: Data Link Layer Error Recovery: ARQ Selective Repeat (or Selective Reject)
Frame 0
ACK 1
Frame 1
Frame 2
SREJ 1
0
0
1
1
2
n=3, W=
Frame 4
Frame 1
ACK 4
0
1
2
Frame 3
2
2
3
3
1
2
3
1
2
3
4
4
ACK 5
Accumulated Acknowledgement
0
1
2
3
SREJ 1
Frame 1
ACK 4
, so drop the frame (late frame)
If there is the minimum retransmission interval is defined, frame1 may not send

## Slide 57: Data Link Layer Error Recovery: ARQ Selective Repeat (or Selective Reject) : Window Size (