## Slide 1: Physical Layer Signal and Modulation
LECTURE 10

## Slide 2: Contents
Signal
Digital Data and Signal
Fourier analysis and Fourier Transform
  Time domain and Frequency domain mapping
Bandwidth and Channel Capacity

## Slide 3: Signal

## Slide 4: Sine Wave
  peak amplitude (A)
  frequency (f)
  phase ()

## Slide 5: Sine Wave
peak Amplitude (A)
  Maximum strength of signal
  typically measured in volts
Frequency (f)
  The number of the signal repetition per second
  Hertz (Hz) = cycles/second
Period (T)
  the amount of time for one repetition
  T = 1/f
Phase ()
  relative position in time within a single period of signal
  radian

## Slide 6: Sine Wave A, f=1/T, 

## Slide 7: Wave Length and Bit Length
the wavelength (
  the distance one cycle occupies on the transmission medium
  Propagation speed x Period (c*T = c/f)
The bit length
  the distance one bit occupies on the transmission medium
  Propagation speed x Bit duration
    Electron propagation speed = 2/3 * c; c = 3x10^8 m/s
    Bit duration = 1/N sec/bit; N = bit rate (bits/sec; bps)

## Slide 8: Digital Data and Signal

## Slide 9: Data Rate vs Signal Rate
Data
  Individual facts, statistics, or items of information
Signal
  An electrical quantity or effect, as current, voltage, or electromagnetic waves, that can be varied in such a way as to convey information
http://www.dictionary.com/

## Slide 10: Data and Signal
Data Rate
  Bits per second (bps)
Signal Rate (baud; Bd)
  Symbol : the unit of signal
  baud is the unit for symbol rate or modulation rate in symbols per second or pulses per second
  It is the number of distinct symbol changes (signaling events) made to the transmission medium per second in a digitally modulated signal or a line code
  If N bits are conveyed per symbol, and the bit rate is R, inclusive of channel coding overhead, the symbol rate fs and the symbol duration time Ts can be calculated as
    ,

## Slide 11: Bandwidth

## Slide 12: Bandwidth
Bandwidth
  The difference between the upper and lower frequencies in a continuous set of frequencies
  It is typically measured in hertz
Passband bandwidth
  the difference between the upper and lower cutoff frequencies of, for example, a band-pass filter, a communication channel, or a signal spectrum
In the case of a low-pass filter or baseband signal, the bandwidth is equal to its upper cutoff frequency

## Slide 13: Bandwidth
Baseband signal
low-pass filter
Passband bandwidth
signal spectrum
communication channel
band-pass filter

## Slide 14: Bandwidth Rough bandwidth approximation of a digital Signal
1/N
T=4/N
T=2/N
T=4/N
270
90

## Slide 15: Bandwidth Rough bandwidth approximation of a digital Signal

## Slide 16: Fourier analysis and Fourier Transform
Composite Signal
Signal mapping between time domain and frequency domain

## Slide 17: Fourier analysis
Jean-Baptiste Joseph Fourier (1768–1830)
  French mathematician and physicist
An arbitrary (continuous) function can be represented by a trigonometric series

## Slide 18: Fourier Transform
the Fourier transform of an integrable function f : ℝ → ℂ
When the independent variable x represents time (with SI unit of seconds), the transform variable ξ represents frequency (in hertz).
Under suitable conditions, f is determined by via the inverse transform:
International System of Units (abbreviated SI)
Xi (uppercase Ξ, lowercase ξ ) /zaɪ/ or /saɪ/
Euler's formula

## Slide 19: Frequency Domain
The frequency domain is more compact and useful when we are dealing with more than one sine wave

## Slide 20: Fourier Transform

## Slide 21: Fourier Transform

## Slide 22: Fourier Transform
An arbitrary (continuous) function = analog signal or square wave
Fourier series of square wave
  Voltage as a function of time
  fundamental frequency (f0=1/T)
    the lowest frequency of a periodic waveform

## Slide 23: Fourier Transform

## Slide 24: Channel Capacity

## Slide 25: Channel Capacity
Maximum rate at which data can be transmitted over a given communications channel under given conditions
  Bandwidth (Hz = cycles per second):
    The bandwidth of the transmitted signal as constrained by the transmitter and the nature of the transmission medium
  Noise: The average level of noise over the communications path

## Slide 26: Channel Capacity Shannon Capacity Formula
Shannon developed formula relating these to signal to noise ratio (in decibels)
  SNRdb=10 log10 (signal/noise)
  capacity C = B log2(1+SNR)
    theoretical maximum capacity
Example
  SNR=3162, B=3KHz
  SNRdb=36, B = 2MHz
    = =

## Slide 27: Channel Capacity Nyquist Bandwidth
In the case of a channel that is noise free
  C = 2B log2L;
    L : signal levels
Example
  L=2, B=3KHz; C=?
    C=2*3K*=6Kbps
  C=265Kbps, B=20KHz; L=?
    = 265K/(2*20K)=6.625; L=98

## Slide 28: Channel Capacity
Example
  B=1MHz, SNR=63; C=? L=?
    = 6M/(2*1M) = 3; L = 8

## Slide 29: Digital Data to Digital Signal
Digital Signal Encoding
1. Line coding

## Slide 30: Digital Signaling Line Coding
Line coding is the process of converting digital data to digital signals
  converting a sequence of bits to a sequence of symbols
Line Coder
Digital
Data
Physical
Waveform
p(t) : Pulse Shape

## Slide 31: Line Coding Nyquist Criterion for Zero–ISI (Inter-Symbol Interference)
power spectral density (PSD)

## Slide 32: Line Encoding Clocking : Bit synchronization
Bit synchronization between the sender and the receiver
  timing of bits - when they start and end

## Slide 33: Line coding Clocking : Bit synchronization
For reliable clock recovery at the receiver, one usually imposes a maximum run length constraint on the generated channel sequence
  the maximum number of consecutive ones or zeros is bounded to a reasonable number

## Slide 34: Line Encoding DC component
DC component : the average voltage over a given interval
  Long term interval
  Short term interval
Causes for non-zero DC component
  Signal polarity
  Disparity of a bit pattern : the difference between the number of transmitted zeros and the number of transmitted ones
    Running disparity : the running total of the disparity of all previously transmitted bits

## Slide 35: Line Encoding Baseline Wander
Since the data is random, the average voltage over a given observation interval will tend to vary with time, causing the base-line to drift randomly
Transmitted signal
Baseline wander W(t)
Received signal
Signal Droop

## Slide 36: Line Encoding Bits per symbol
Data element (Unit of Data) :
  Bit; bps (bits per second)
Signal element (Unit of Signal) :
  Symbol; baud (symbols per second)
  Signal bandwidth

## Slide 37: Line coding Bits per symbol
Bit to signal ratio (r)
  N bits → M signals
  r = N/M (bits per symbol)
Baud (Signal Rate)
  R = data rate (bps)
  =
  Example:
    (b) 1 bit → 2 signals, r=1/2, = 2*R (bandwidth)
    (c) 2 bits → 1 signals, r=2/1, = *R (bandwidth )

## Slide 38: Line coding Good line coding criteria
Minimize transmission hardware
Facilitate (bit) synchronization
Minimize bandwidth
Eliminate a dc component (long term dc effect)
Minimize baseline wandering (short term dc effect)
Transparency
  Any arbitrary symbol pattern can be transmitted and received
Ease error detection and correction
Lower Bit Error Rate (BER) performance
  Signal level : two-level coding schemes have better BER than three-level coding schemes

## Slide 39: Line Encoding Power Spectrum Density (PSD)
The power spectrum density of a line code describes the distribution of power into frequency components composing that signal
A digital signal is a composite analog signal with infinite bandwidth
  The power spectral density (PSD) refers to the spectral energy distribution that would be found per unit time, since the total energy of such a signal over all time would generally be infinite

## Slide 40: Line Encoding Power Spectrum Density
PSD
  DC component (long term DC effect)
    A spike at 0 Hz
  Baseline Wander (short term dc effect)
    High PSD at low frequency (or 0 Hz)
  Bandwidth (Baud)

## Slide 41: Line coding mapping concept
Data only : {1,0}
Data + Clock : {1,0} + clock signal
  Clock signal : transition in the bit period

## Slide 42: Line coding mapping concept
Signal :
  Amplitude : {high-level, low level}
    Polarity
      {1,0} : Unipolar {+V,0} , Polar {+V, -V } , bipolar {V, 0}
  Alteration of amplitude
    Alternative Mark Inverted (AMI) {mark(V), 0}
      The number of Ones transmitted : even (+V), odd(-V)
      Bit error detection
  Transition of amplitude
    Differential coding
      the beginning of the bit period : { transition, non-transition}
      the middle of the bit period : { down transition, up transition }

## Slide 43: Line coding Unipolar RZ and NRZ
Return to Zero (RZ)
Non Return to Zero (NRZ)
Power Signal Density (PSD)
DC component
r = ½, Baud=2N
DC component
R=1, Baud=N
Baseline wander
clocking
No clocking
No transparency : 0000… or 111111 and no error detection

## Slide 44: Line coding Polar RZ and NRZ
Polar RZ
Polar NRZ (NRZ-L)
Power Signal Density (PSD)
No transparency : 0000… or 111111 and no error detection
No DC component
r = ½, Baud=2N
No DC component
R=1, Baud=N
Baseline wander
clocking
No clocking

## Slide 45: Line coding Polar RZ and NRZ
Polar NRZ-M (NRZ-I) and Polar NRZ-S
1 does nothing (keeps sending the previous level) 0 forces a transition
1 forces a transition 0 does nothing (keeps sending the previous level)
NRZ-L (Level)
NRZ-M (mark)
NRZ-S (Space)

## Slide 46: Line coding Bipolar RZ and NRZ
Bipolar RZ (RZ-AMI)
Bipolar NRZ (NRZ-AMI)
Power Signal Density (PSD)
Not transparent : 0000… and single bit error detection
No DC component
r = ½, Baud=2N
No DC component
R=1, Baud=N
clocking
No clocking
Alternative Mark Inverted (AMI) {mark(V), 0}

## Slide 47: Line coding Manchester encoding
Manchester encoding (Polar Biphase-L)
Differential Manchester encoding
OR
Example
https://en.wikipedia.org/wiki/Line_code
1 keeps level constant 0 forces a transition
A transition in the middle of the bit
1 forces a negative transition in the middle of the bit 0 forces a positive transition in the middle of the bit
Two consecutive bits of the same type force a transition at the beginning of a bit period. 0 forces a negative transition in the middle of the bit 1 forces a positive transition in the middle of the bit
R=1/2, Baud=2N
No DC component
Transparent
No error detection

## Slide 48: Line coding BER : two-level & three-level line coding
dB = 10*
3dB=10*
= =1.995
2
Eb/N0 (SNR per bit)
energy per bit to noise power spectral density ratio
a normalized signal-to-noise ratio (SNR) measure
when comparing the bit error rate (BER) performance of different digital modulation schemes without taking bandwidth into account

## Slide 49: Digital Data to Digital Signal
Digital Signal Encoding
2. Multilevel Coding

## Slide 50: Multilevel Coding 2B1Q
2B1Q
  2 bits are mapped to a single signal having 4 states {-3, -1, +1, +3}
2B1Q Table (Gray code)
00 -3
01 -1
+1
10 +3

## Slide 51: Multilevel Coding 8B6T
8B6T (243()<256()<729() states)
  8 bits are mapped into 6 signal symbols using the mapping table
    Each symbol has three states {-V,0,+V}
  100BASE-T4 (obsoleted) used 8B6T

## Slide 52: Multilevel Coding MLT-3 encoding
MLT-3 cycles sequentially through the voltage levels −1, 0, +1, 0.
It moves to the next state to transmit a 1 bit, and stays in the same state to transmit a 0 bit
MLT-3: Multi-Level Transmit

## Slide 53: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
Four dimensional five-level pulse amplitude modulation (PAM)
  Signal level : { -2, -1, 0, +1, +2 }
    X = {-1, +1}, Y= { -2, 0, +2 }
{-2,-1,0,+1,+2}
{-2,-1,0,+1,+2}
{-2,-1,0,+1,+2}
{-2,-1,0,+1,+2}
{X, Y}
{X, Y}
{X, Y}
{X, Y}
States = 5x5x5x5 = 625
625 states are grouped into 16 subsets. (16 = 2x2x2x2)
16 subsets are grouped into 8 subsets again.
Each subsets chooses 64 states (8*64=512=2^9)
2x2x2x2+3x3x3x3
=16+81=97
Subsets = 2x2x2x2 = 16
2x3x2x2+3x2x3x3
=24+54=78

## Slide 54: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
The combined output of all four transmitters on each line forms a four-dimensional constellation.
  the possible outputs of each transmitter as an axis orthogonal (at right angles () to the other axis.
https://www.iol.unh.edu/sites/default/files/knowledgebase/ge/pcs.pdf

## Slide 55: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
For every symbol period, one point in the constellation is sent.
  While the real system is a 5x5x5x5 constellation,
  A simple 5x5 constellation is easier to explain…
Line 1 (+1)
(-2)
Line 2
Line 3 (+2)
(-1)
Line 4

## Slide 56: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
However, noise affects the constellation.
  If too much noise disrupts the signaling, then the receiver will not be able to distinguish between the correct point in the constellation and neighboring (incorrect) points in the constellation.
Attenuation also affects the constellation, with similar concerns.
https://www.iol.unh.edu/sites/default/files/knowledgebase/ge/pcs.pdf

## Slide 57: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
Increasing Symbol Distance
  To combat this problem, limit the permissible combination of symbols.
  The separation of “even” and “odd” points has the effect of increasing the minimum distance between the permissible transmit codes.
  The minimum squared distance = = 2
https://www.iol.unh.edu/sites/default/files/knowledgebase/ge/pcs.pdf
1
2

## Slide 58: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
It can be shown that the minimum squared distance between any two points in a sublattice (a subset) is at least 4.
Example
  D4: XYYX + YXXY
  Pick +1(X),-2 (Y),+2 (Y),-1 (X) and 0 (Y),-1(X),+1(X),0 (Y)
  The minimum squared distance:
    = 1+1+1+1=4
  D0: XXXX + YYYY
  Pick -2, -2, 0, -2 and 0,0,-2,0
  The minimum squared distance:
https://www.iol.unh.edu/sites/default/files/knowledgebase/ge/pcs.pdf

## Slide 59: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s) Trellis Encoder
Subset
Selector
(= 8)
Point selector within the subset
(= 64)
Encoder: Trellis-Coded Modulation [TCM] (a kind of BCC)
Decoder: Viterbi Algorithm

## Slide 60: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s) The 1000BASE-T Convolutional Encoder
IEEE 802.3-2022 40.3.1.3.4 Generation of bits Sdn[8:0]
- The figure taken from the reference
https://www.iol.unh.edu/sites/default/files/knowledgebase/ge/pcs.pdf
Enabled(1)

## Slide 61: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s) The Trellis Structure of the encoder
https://www.iol.unh.edu/sites/default/files/knowledgebase/ge/pcs.pdf
Sdn[6..7]=00
Sdn[6..7]=01
Sdn[6..7]=10
Sdn[6..7]=11
CSn[0..2]
Before
CSn[0..2]=000
Input: Sdn[6..7] = 01
CSn[1] = CSn[0]Sdn[6]= =0
CSn[2] = CSn[1]Sdn[7]= =1
After
CSn[0..2]=001

## Slide 62: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
IEEE 802.3-2022 Table 40–1—Bit-to-symbol mapping (even subsets)

## Slide 63: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
IEEE 802.3-2022 Table 40–1—Bit-to-symbol mapping (even subsets) (continued)
Code (2’s complements)
010 (+2)
001 (+1)
000 (0)
111 (-1)
110 (-2)
Coded output
(-2,-2,-2,+2)→(110 110 110 010)

## Slide 64: Multilevel Coding 4D-PAM5 (Ethernet 1Gb/s)
m=8bits
m+r=8bits+1bit
r=TCM bit (parity)
Pn= 4*(3bits); 3bits for PAM5
- 3bits indicates one of { -2, -1, 0, +1, +2 }
4 channels (125Mbaud) = 4 X 125Mbaud
256 states
512 () states = sd[6..8] x sd[0..5]= 8 x 64 = () subgroups x () points
Each state is represented by 12bits (4*3bits): 9bits→12bits
– Only 512 valid codes among 4096 codes
Each selected point (12bits) is mapped to four 3 bits outputs for four wire
R=1Gbps, r=8bits per 4symbols= 2bits per 1symbol per channel,
; 1000BASE-T (1GBASE-T)
8bits←(Viterbi Decoder)←9bits←(Constellation Demapper) ←12bits

## Slide 65: Input Data Randomization
1. Scrambling

## Slide 66: Input Data Conversion
Problem
  Transparency
    Any arbitrary symbol pattern can be transmitted and received
    00000000….. or 11111111….
  DC component
    Long term Disparity (Running disparity)
  Baseline wander
    Short term Disparity
Solution
  Input data conversion or randomization
    Running Disparity (RD) to be (near) zero
      the running total of the disparity of all previously transmitted bits
      The difference between the number of Ones and the number of Zeros in a data
    Distribution of Ones and Zeros to be even

## Slide 67: Input Data Conversion
Code Mapping
  Block Code : m-to-n bits mapping
Substitution of pre-defined input pattern
  Replacing continuous zeros (8/4) to pre-defined pattern
Scrambling
  Pseudo-random generator
    a linear feedback shift register (LFSR)
      An LFSR of ‘n’ elements will identically repeat its output every -1 outputs

## Slide 68: Code Mapping : Block Coding
Block coding
  adding the redundancy to ensure synchronization and to provide some kind of inherent error detecting

## Slide 69: Input Data Conversion Block Coding : 4B5B
4B5B maps groups of 4 bits (quadbits) onto groups of 5 bits, with a minimum density of 1 bits in the output
  each block of 4 consecutive bits an equivalent word of 5 bits
  5 bit words are pre-determined in a dictionary and
  they are chosen to ensure that there will be at least two transitions per block of bits

## Slide 70: Block Coding
4B5B encoder with NRZ-I (Polar NZR-M) line coder
100BASE-TX

## Slide 71: Input Data Conversion Block Coding : 8B10B
8b/10b maps 8-bit words to 10-bit symbols to achieve DC-balance and bounded disparity, and yet provide enough state changes to allow reasonable clock recovery
  the difference between the counts of ones and zeros in a string of at least 20 bits is no more than two, and
  there are not more than five ones or zeros in a row

## Slide 72: Input Data Conversion Block Coding : 8B10B
5B/6B
3B/4B
EDCBA
HGF
iedcba
jhgf
6B/4B = N[1]-N[0] = 2,0
- 6B: 00+1111, 0000+11, 000+111
- 4B: 0+111,000+1, 00+11
Initial RD (Running Disparity) = -1

## Slide 73: Substitution of pre-defined input pattern
Replacing continuous zeros (8/4) to pre-defined pattern

## Slide 74: Input Data Conversion Substitution of pre-defined input pattern
Replacing pre-defined input bits to another input bits having the same length
  no dc component
  no long sequences of zero level line signal
  no reduction in data rate
  error detection capability

## Slide 75: Modified AMI code : B8ZS
Bipolar NRZ (NRZ-AMI)
bipolar with eight-zero substitution (B8ZS)
  replacing each string of 8 consecutive zeros with the special pattern "000VB0VB“
    the polarity of the preceding mark (1)
      Positive(+) : 000+−0−+
      Negative(-) : 000−+0+−

## Slide 76: Modified AMI code : HDB3
high density bipolar of order 3 (HDB3)
  replacing any instance of 4 consecutive 0 bits with one of the patterns "000V" or "B00V"

## Slide 77: Modified AMI code : HDB3

## Slide 78: Scrambling
Input XOR with Pseudo-Random bit strings
In XOR PR = Out; 1010 XOR 1100 = 0110
Out XOR PR = IN; 0110 XOR 1100 = 1010

## Slide 79: Input Data Conversion Scrambling
  Input data is randomized by XOR with input data and the output of a pseudo-random generator
  Pseudo-random generator
  a linear feedback shift register (LFSR)
    An LFSR of ‘n’ elements will identically repeat its output every -1 outputs

## Slide 80: Scrambling a linear feedback shift register (LFSR)
The repeating 7-code () pattern for this LFSR (n=3)
(TTT:111) 0010111
TTT:111: Output:0
TTT:011: OutPut:0
TTT:001: OutPut:1
TTT:100: OutPut:0
TTT:010: Output:1
TTT:101: Output:1
TTT:110: OutPut:1
-------------------------
TTT:111: Output:0

## Slide 81: Scrambling Example
(1111) 1
(0111) 1
(1011) 1
(0101) 1
(1010) 0
(1101) 1
(0110) 0
(0011) 1
(1001) 1
(0100) 0
(0010) 0
(0001) 1
(1000) 0
(1100) 0
(1110) 0
(1111)

## Slide 82: Scrambling 1000BASE-T Scramblers
Auto-Negotiation in Physical Control
-1 (8589934591) bits before the LFSR pattern repeats (68.72s)

## Slide 83: Digital Data to Analog Signal
Digital Modulation (Shit Key)

## Slide 84: Signaling Scheme Basic Concepts : Sine Wave
;
  peak amplitude (A)
    Amplitude Shift Key
  frequency (f)
    Frequency Shit Key
  phase ()
    Phase Shift Key
  peak amplitude (A) + phase ()
    Quadrature Amplitude Modulation (QAM)
  frequency (f) + phase ()
    Minimal Shift Key (MSK)

## Slide 85: Signaling Scheme Basic Concepts

## Slide 86: Signaling Scheme Basic Concepts : Orthogonal functions
Periodic Functions
  f(x+T)=f(x) for all X; T = Period of f(x)
  ) and with T =
  f and g are both periodic functions with period T
    f+g & fg are periodic
Even and Odd Functions
  Even function : f(-x)=f(x); cos(x)
  Odd function : f(-x)=-f(x); sin(x)

## Slide 87: Signaling Scheme Basic Concepts : Orthogonal functions
Orthogonal Functions
  Two non-zero functions are orthogonal on a x b if
    the integral of the product of functions over the interval
  A set of non-zero functions are mutually orthogonal on a x b if

## Slide 88: Signaling Scheme Basic Concepts : Orthogonal functions
See http://tutorial.math.lamar.edu/Classes/DE/PeriodicOrthogonal.aspx for proof

## Slide 89: Signaling Scheme Basic Concepts : Euler's formula
Euler's formula
  the fundamental relationship between the trigonometric functions and the complex exponential function
Euler's Identity : +1 = 0
=
-
https://www.youtube.com/watch?v=BH0snUYPQEM

## Slide 90: Signaling Scheme Basic Concepts : Euler's formula
Relationship to trigonometry
  an interpretation of the sine and cosine functions as weighted sums of the exponential function

## Slide 91: Amplitude Sift Key (ASK) Binary ASK : On-Off keying (OOK)
the amplitude of the carrier signal is varied to create signal elements.
Both frequency and phase remain constant

## Slide 92: Amplitude Sift Key (ASK) Demodulation
=
energy per bit
: bit duration

## Slide 93: Frequency Shift Key
The frequency of the modulated signal is constant for the duration of one signal element, but changes for the next signal element if the data element changes
Both peak amplitude and phase remain constant for all signal elements

## Slide 94: Frequency Shift Key
=
If
Coherent detection
energy per bit
: bit duration

## Slide 95: Phase Shift Key (PSK)
the phase of the carrier is varied to represent two or more different signal elements

## Slide 96: Phase Shift Key (PSK) Binary PSK (BPSK)
= -
= =
=
energy per bit
: bit duration

## Slide 97: Phase Shift Key (PSK) BPSK constellation diagram
BPSK Constellation

## Slide 98: M-ary Signaling Scheme
M-ary Signaling Scheme
  M states (symbol states)
    The “off” states
    M-1 discrete “on” states
  Bit rate bps (bit peiod: )
    Symbol rate (symbols per second)
      ;
      Symbol period () = 1/
    Transmission Bandwidth (Hz)
  Spectral Efficiency
    bps/Hz

## Slide 99: M-ary Signaling Scheme Quadrature phase-shift keying (QPSK)
QPSK can encode two bits per symbol, shown in the diagram with Gray coding to minimize the bit error rate (BER)
QPSK can be used to double the data rate compared with a BPSK system while maintaining the same bandwidth of the signal

## Slide 100: M-ary Signaling Scheme Quadrature phase-shift keying (QPSK)
Writing the symbols in the constellation diagram in terms of the sine and cosine waves used to transmit them:
When transmitting two signals by modulating them with QPSK(QAM), the transmitted signal will be of the form:

## Slide 101: M-ary Signaling Scheme Quadrature phase-shift keying (QPSK)
/
/
/
/
dt =
dt =
energy per bit
: bit duration

## Slide 102: M-ary Signaling Scheme Quadrature phase-shift keying (QPSK)
QPSK Constellation
Writing the symbols in the constellation diagram in terms of the sine and cosine waves used to transmit them:
= -
= -
-
= I(t)- Q(t)

## Slide 103: Gray Code
A Gray Code represents numbers using a binary encoding scheme
  It groups a sequence of bits so that only one bit in the group changes from the number before and after
Binary Reflected Code (Frank Gray; 1947)
https://www.allaboutcircuits.com/technical-articles/gray-code-basics/
0
7

## Slide 104: M-ary Signaling Scheme Quadrature Amplitude Modulation (QAM)
Order G[0..3] I Q
0000 00 00 -3 -3
0001 00 01 -3 -1
0010 00 11 -3 +1
0011 00 10 -3 +3
0100 01 10 -1 +3
0101 01 11 -1 +1
0110 01 01 -1 -1
0111 01 00 -1 -3
1000 11 00 +1 -3
1001 11 01 +1 -1
1010 11 11 +1 +1
1011 11 10 +1 +3
1100 10 10 +3 +3
1101 10 11 +3 +1
1110 10 01 +3 -1
1111 10 00 +3 -3
constellation

## Slide 105: M-ary Signaling Scheme Quadrature Amplitude Modulation (QAM)
I(t)=3, Q(t)=1, K=
=